## Slide 1: CANARY
The LGS AO Demonstrator at the WHT
Tim Morris (Durham University)
and
The CANARY team

## Slide 2: Contents
Tomography in Adaptive Optics
Multiple Object Adaptive Optics
CANARY Status and Results
Impact on future AO systems

## Slide 3: Adaptive optics
Technique for the correction of images distorted by the passage of light through a turbulent medium
Restores telescope resolution, concentrates light to allow shorter exposures
Before AO
After AO

## Slide 4: AO Systems to date
First generation systems suffered from low sky coverage and narrow field of view
  Complex to use and understand
  Still produced interesting (if sparse) results
Second/third generation systems improved sky coverage (LGS), more reliable and were able to cope with varying atmospheric conditions.
Field of view remains a problem…
1
2
3
See e.g. Ghez et al ApJ 689, 1044 (2008)
Genzel et al, Nature 442, 786-789 (2006)
Marchis et al, Icarus 176, 96-122 (2002)

## Slide 5: How does tomography help AO?
Closed loop control

## Slide 6: How does MOAO differ?
Open loop control

## Slide 7: CANARY Project
Create a single MOAO channel (resembling EAGLE as closely as possible) using the 4.2m William Herschel Telescope
  Effectively a 1/10th scale model of E-ELT using 4x 10km Rayleigh LGS to emulate >80km Na LGS
Perform NGS, then LGS based tomographic WFSing
Perform open-loop AO correction on-sky
Develop calibration and alignment techniques
Fully characterise system and subsystem performance
No requirement to deliver astronomical science

## Slide 8: Phase A : NGS MOAO
Components:
  Low-order 8x8 DM
  3 x L3CCD open-loop NGS WFSs
  Open-loop optimised Fast Steering Mirror
  Hardware accelerated Real Time control system
  NGS MOAO Calibration Unit
WHT
Nasmyth
Calibration Unit
NGS Pickoffs
3 x NGS WFS
NGS FSM
Low-order DM
Science Verification
Truth Sensor
Figure Sensor
GHRIL Derotator
Phase A: NGS MOAO
NGS WFS
NGS WFS
NGS WFS
10" science FOV
2.5’ Derotated WHT field

## Slide 9: Strehl ratio comparison image
Seeing-limited (NoAO) (SR=1% at 00h59mn)
GLAO (SR=9% at 00h42mn)
MOAO (SR=19.4% at 00h29mn)
SCAO (SR=23.8% at 00h32mn)
Images recorded at a central wavelength of 1.495µm

## Slide 10: Terms of the error budget
σ2tomo
Tomographic error
σ2OL
Open loop error (go-to error)
σ2tomonoise
noise propagated throught reconstructor on the DM
σ2aliasing
Aliasing correlated (ground) and not correlated (alt)
σ2BW
Bandwidth error (temporal error)
σ2fitting
Fitting error
σ2statbench
internal Strehl (best SR on bench without turbulence)
σ2static
MOAO measured telescope+Canary field static aberrations
σ2others
σ2noiseTS
Noise on Truth Sensor
???

## Slide 11
From synchronised data at 00h10mn12s (Asterism #47)
Error | Estimated value (nm rms)
σ2tomo | 168
σ2OL | 68
σ2tomonoise | 48
σ2aliasing | 71
σ2BW | 88
σ2fitting | 137
σ2statbench | 150
σ2static | 77
Total | 308
r0=16.3cm (0.69’’ seeing)
7 seconds of data (fe=150Hz)
Expected SR = 19.0%@1.49µm => measured = 21%

## Slide 12: Phase B: Low-order LGS MOAO
Adds four open-loop LGS WFSs to the existing three NGS WFSs
Can run in LGS or NGS modes or a mixture of both
Crucial for demonstrating EAGLE
WHT
Nasmyth
Calibration Unit
NGS Pickoffs
3 x NGS WFS
NGS FSM
Low-order DM
Science Verification
Truth Sensor
LGS Pickoffs
4 x LGS WFS
GHRIL Derotator
Figure Sensor
Lasers
LGS Rotator
GLAS BLT
Diffractive Optic
LGS
FSM
LGS Dichroic
Phase B: Low-order LGS MOAO
LGS WFS
1.0’ Diameter LGS asterism

## Slide 13: March/april 2012 commissioning

## Slide 14: March/April 2012 commissioning
LGS launch system commissioned without full CANARY system
Test setup at the Nasmyth platform
Interfaces to telescope (beam steering, beam combination, launch system control, safety) commissioned
4 x LGS WFS optics tested
Single LGS Pockels cell range gate shutter tested
LGS fratricide for a 4 guide star asterism mapped
Cloud layers
Diffraction spikes from LGS asterism generator

## Slide 15: Phase B Status
System has been run on the bench using 1-3 NGS and/or 1-4 LGS
New range-gated detector ordered
Initial experiments will be run with 2-3 x NGS and 1 x LGS
  LGS can be positioned anywhere in the field for testing tomography
Laser launch system tested and interfaced to the WHT
2 nights on sky at the end of July
10 further nights between August and November
Being packed in Paris as I speak and shipped to La Palma on Friday…
But Phase B still doesn’t fully demonstrate MOAO in an E-ELT like configuration…

## Slide 16: CANARY Phase C
Reconfiguration of the Phase B system to produce a system closely resembling the proposed EAGLE configuration
Tip/tilt, focus
High orders
T
E
L
E
S
C
O
P
E
TS
DM
Tip/tilt, focus
High orders
3
NGS
WFS
4
LGS
WFS
IR CAM

## Slide 17: CANARY Phase C1 (2013/14)
GLAO/LTAO/SCAO
Tip/tilt, focus
High orders
T
E
L
E
S
C
O
P
E
TS
DM
3
NGS
WFS
4
LGS
WFS
IR CAM

## Slide 18: CANARY Phase C2 (2014+)
MOAO/LTAO/GLAO/SCAO
Tip/tilt, focus
Low orders
T
E
L
E
S
C
O
P
E
TS
DM
High orders
3
NGS
WFS
4
LGS
WFS
IR CAM
DM
High orders

## Slide 19: Why is this important now?
LGS-MOAO and LTAO haven’t been demonstrated
The E-ELT won’t work without AO
  Telescope vibrations, structure induced turbulence, etc., will mean you have to run with AO to get an image
  Even the active optics system is a 5-layer multi-conjugate system…
List of untested/untried techniques essential to E-ELT operation will be developed using CANARY is large…
    Open-loop wavefront control
    Pseudo open-loop tomography
    Effect of LGS fratricide and elongation under controlled conditions
    Split closed-loop woofer/open-loop tweeter control
    On-sky calibration techniques
    On-sky algorithm testing
    Mixed LGS/NGS tomography
    On-line turbulence profiling and system optimisation
    More…

## Slide 20: How Does CANARY help?
CANARY is the only on-sky capable system in the world that has the same multi-DM + WFS configuration that is proposed for the E-ELT
It is the only AO system that can be reconfigured to add/remove hardware subsystems
Linux-based real-time control system allows easy implementation of new software/algorithms.
All of this is made possible by the unique infrastructure present at the WHT
    Large enough telescope to do tomography
    Large, gravity stable Nasmyth platform
    Laser guide star launch system
New collaborations (since Phase A results published) started with
    INAF Arcetri (LGS Pyramid wavefront sensors)
    Observatoire de Lyon (Fractal Iterative Method for wavefront reconstruction)
    ONERA/L2TI (LQG wavefront control)
    ESO/ATLAS team (Driver behind C1 configuration)
    ESO (Sodium LGS elongation study)
    GranTeCan (WFS interfacing and real-time control)

## Slide 21: Conclusions
CANARY has shown that open-loop tomography works
  Predicted and actual on-sky performance match well (more work to be done on the comparisons though!)
  Error budget is complicated
Phase B will be on-sky in under 2 months and demonstrate split NGS/LGS tomography
CANARY installed at the WHT is the only system in the world that can perform on-sky investigation of many of the unsolved issues relating to E-ELT telescope and future AO instrument design

## Slide 22: The CANARY team
Durham | Richard Myers, Gordon Talbot, Nigel Dipper, Deli Geng, Eddy Younger, Alastair Basden, Colin Dunlop, Nik Looker, Tim Butterley, Laura Young, Simon Blake, Sofia Dimoudi, Paul Clark, Nazim Bharmal, Richard Wilson Harry Shepherd
Observatoire de Paris | Zoltán Hubert, Gerard Rousset, Eric Gendron, Fabrice Vidal, Damien Gratadour, Aglae Kellerer, Michel Marteaud, Fanny Chemla, Phillipe Laporte, Jean-Michel Huet, Matthieu Brangier, Olivier Martin, Mathieu Cohen
UKATC | Andy Longmore, David Henry, Stephen Todd, Colin Dickson, Brian Stobie, David Atkinson
ONERA | Jean-Marc Conan, Gaetano Sevo, Thierry Fusco, Clelia Robert, Nicolas Vedrenne
ING | Jure Skvarc, Juerg Rey, Neil O’Mahoney, Tibor Agocs, Diego Cano, Don Carlos Abrams
PUC Santiago | Andres Guesalaga, Dani Guzman
L2TI | Caroline Kulscar, Henri-Francois Raynaud
Engineering and Project Solutions Ltd | Kevin Dee
The CANARY project is supported via the following funding bodies
  STFC
  UK E-ELT Design Study
  EU FP7 Preparatory fund WP9000
  ANR Maui, INSU, Observatoire de Paris
  FP7 OPTICON JRA1